## Slide 1: MODULAR BUSINESS PROGRAM TRUCKS Orientation for Sales Training Team
MBP TRUCKS
01st August 2019

## Slide 2: Program Vision
To be in the Global Top 10 in M&HCV Trucks (>7.5T GVW) and Global Top 5 in M&HCV Buses (8m and above)
in volume terms.
Deliver profitability through customized solutions significantly faster.
Deliver the vision efficiently by lowering complexity to
Manufacture efficiently
Source more effectively
Enhance aftermarket revenues
Improve serviceability
Company Vision
MBP Vision
To achieve market leadership in the Domestic market.
To target one-fourth of volumes from International markets.
Trucks BU Vision

## Slide 3: Lego Principle in Modularity
Lego Principle is adopted to achieve modularity for getting more vehicle variants
By using 3 simple Lego pieces, a variety of shapes can be formed.

## Slide 4: MODULE MODULARITY – VARYING MODULE
Fixed Module
Variable module

## Slide 5
Common Front Module Aggregates For MVP Variants – 4X2,6X4,8X4 & 10X4
Fuel filter
DDU
Purge tank
Compressed air cooling coil
Cooling system
Engine position
CSO
Air cleaner
Steering Reservoir
Steering box
Front cab mount

## Slide 6
Fuel system common interface
Cooling system common interface
Exhaust system
common interface
Cooling system
common interface
Front Module Interface

## Slide 7
FVDP-N
Different Engine position
BT height of cab
H6
N4
N6
H4
N4
H6
N6
ISME
All Engines packaged in common flywheel housing position
MVP
POSITION MODULARITY– Common Engine Position
Common Engine Position
251
215
564
385
385
430
305
CTTP
Ecomet
NGICV
All possible aggregate to be checked for packaging arrangement to increase the interchangeability
e.g: MVP 4 type of front axle checked with 5 type of engine sumps.
Notes: 7

## Slide 8: Engines (160hp to 360hp)
H6 engine
N4 engine
N6 engine

## Slide 9: Cabin
NGC family
G91 family
Features
Common Looks
Metal bumper
All-Metal front facia

## Slide 10
Easy conversion to different vehicle configurations
Eg 4x2 to 6x4
Changes involved will only be frame, Rear Module - rear electrical module and rear air piping module
Various Wheelbases in 50 mm increments with minimal vehicle changes without change in front module and load module
MODULE MODULARITY – VARYING MODULE

## Slide 11: MODULE MODULARITY – WHEEL CONFIGURATION
4x2 4x4 6x4 / 6x2 / 6x2(4/2) 6x6 6x2P 8x2P(2) / 8x4P(2) 8x4(4/2) / 8x4(4) 8x6P(2) / 8x8(4) 10x2P(4) / 10x4P(4) / 10x6P(4) 12x4P(6/2)
RHD
LHD
All vehicle configurations from 4x2 to 12x4 possible
Modular Layout between LHD and RHD
Front module remaining same, the changes required to extend the vehicle family (wheel base) is very minimal

## Slide 12
SPLIT MODULARITY – Electrical wiring
red : series COMMON CABLE dotted : engine & battery COMMON CABLE
Cable colours legend:
CE
BR
CG
FC
FB
C_rear
+
BATTERY
BL
C9
Wheel Base 1
Rear Cable 1
BASIC RANGE
Basic Functions:
Front lights
Rear lights
Trailer lights
Engine ECU
Alternator
Engine start motor
Fuel level
Gearbox signals
Power distributions

## Slide 13
CE
BR
CG
FC
FB
C_rear
+
BATTERY
BL
Wheel Base 2
Rear Cable 2
red : series COMMON CABLE dotted : engine & battery COMMON CABLE
Cable colours legend:
Basic Functions:
Front lights
Rear lights
Trailer lights
Engine ECU
Alternator
Engine start motor
Fuel level
Gearbox signals
Power distributions
BASIC RANGE
C9
SPLIT MODULARITY – Electrical wiring

## Slide 14: Pneumatic piping module interface

## Slide 15
SPLIT MODULARITY – Air piping
Front module wiring
Rear module wiring
Module base design to reduce the part number and inventory
Cost effective connector concept for air piping

## Slide 16
190
NGC/FVDP2 chassis
692
NGC /FVDP N chassis
POSITION MODULARITY – Air intake system

## Slide 17
Existing Design : Weight - 290Kgs
Trunnion Shaft
(63 Kgs)
Bogie Cross member
(85.3 Kgs)
Bogie Brackets
(52 Kgs x 2)
Radius rod Mounting brackets (9.5 Kgs x 4)
Single Piece Bogie Bracket
Proposed Design : Weight - 230Kgs
Advantages :
1.Lesser weight & cost
2. Lesser number of parts and hence assembly time reduction
3. Lesser fasteners and easy maintenance
4 .Lesser failure modes
INTEGRATION MODULARITY – BOGIE SUSPENSION

## Slide 18
INTEGRATION MODULARITY – FRONT NODO BRACKET

## Slide 19
Same  Top Cover | Varying depth Bottom Cover | Different Air Cleaner sizes | Capacity (m3) | Engine
 |  |  | 12-15 | H4-N4
 |  |  | 15-18 | N4-H6
 |  |  | 21-24 | N6-Higher power
SYSTEM MODULARITY – Air intake cleaner

## Slide 20
200 L
160 L
120 L
80 L
Left
Module
Right
Module
Centre
Module
SYSTEM MODULARITY – Exhaust muffler

## Slide 21
DIMENSIONAL MODULARITY – Frame hole pattern

## Slide 22
Total variant of FSM section : 4x3 = 12 (variant)
4mm
5mm
6mm
180 mm
225 mm
270 mm
315 mm
Modular Frame web height of 180, 225, 270 & 315mm to suit LMH Series
5mm
6mm
7mm
7mm
8mm
9mm
45
HEIGHT MODULARITY – Frame section height
45
50

## Slide 23
HEIGHT MODULARITY – Cooling system radiator
Varying
height
570
680
800
1130
1256

## Slide 24: Modular Frame & Cross Member Strategy in MVP
Heavy
Light
Single piece X Member
H = 225 T = 5, 6, 7
H = 315 T = 7, 8, 9
H = 185 T = 4, 5, 6
H = 270 T = 7, 8, 9
Reduced Vehicle Weight
Cost Reduction
Reduced Number of Parts
Reduced Assembly Time
Less Failure Modes
PROFILE MODULARITY- Frame architecture
Medium
Light, Medium &
Heavy

## Slide 25
Existing- Rear Suspension with helper spring and helper spring brackets. More no.of parts
Proposed- Rear Suspension without helper spring and helper spring brackets. Reduced no.of parts.
ELIMINATION MODULARITY – Rear suspension

## Slide 26
FSM drawing and CAD visualization
without Drawing Modular Approach
FSM drawing and CAD visualization
with Drawing Modular Approach(FSM Modules)
DRAWING MODULARITY – Frame side member

## Slide 27
FRONT AXLE
Foundation Brake Group Front
Level 1
Brake Actuation front
Level 1
BRAKES
Foundation Front axle
Level 1
Wheel Hubs – Front
Level 1
Steering Linkages Group – Front
Level 1
Brake type
Brake Size
Bearing Type
Axle geometry
Wheel Base Wheel Track
GVW
Axle Conf.
Terrain
Current – Assembly Group
MVP –
Functional Groups
FRONT AXLE
A No – Level 1
GVW
Application
Slack Adjuster type
GVW
Axle Conf.
Terrain
Wheel base
Wheel Track
Application
Brake Type
Bearing Type
Slack Adjuster type
GVW
Brake type
BOM MODULARITY – Front axle system

## Slide 28
Foundation front Axle | Wheel hub Group Front | Foundation Brake Group Front | Brake Actuation front | Steering Linkages Group
FA99 | Hub 6” & 7” | Brake 7” | Type 20 | SL 1645 TRL
 | Hub 8” | Brake 8” | Type 24 | SL 1705 TRL
1 | 6 | 5 | 7 | 8
FA99 with 8” brake for short WB
Example:- FA99 Variants
Total ~192 combination with 27 variants in 5 modules
FA99 with 7” brake for long WB
BOM MODULARITY – Front axle system

## Slide 29
Product Configurations
Product Configuration Features
  Right Product for the Application and Operating conditions
  Product based on Load / Road conditions
  Aggregate configurations
  Suspension configurations
  Tyre configurations
  Cabin configurations and levels

## Slide 30: MBP Models – 4X2 Haulage
Sub-Segment
Loading Span
Engine Power
GB Config’n
Suspension-Frt
Suspension-Rear
Cab
Fuel Tank
Load Road
4X2
18 ft
200HP H6
S6 36 DD
SemiEllipt 7000kg
Semi Ellipt 11500kg
G91 S
220 litres
L1*R1, L2R1, L2R3, L3R1, L4R1
20 ft
6MT 86
SemiEllipt 8000kg
Semi Ellipt 16000kg
WIM Eco/ Std
300 litres
L1*R1, L3R1, L3R3,L4R1
22 ft
Parabolic 7000kg
WSM Eco/ Std/ Dlx
375 litres
L1*R1, L3R3
24 ft
Parabolic 8000kg
New FES
Dual Tank
+220Litres
L1*R1
26 ft
Parabolic 10500kg
Dual Tank
+300Litres
L1*R1
28 ft
Dual Tank
+375Litres
L1*R1
30 ft
L1*R1
32 ft
L1*R1, L2R1
Applications
4x2 Model for POL application will be released separately,
ULW
M –6223
CT –5165
U –
B – 5170 (BS6)
M –6251
CT –
U –
N -
M –6279
CT –
U –
N -
M –6307
CT –
U –
N -
M –6335
CT –
U –
N -
M –6363
CT –
U –
N -
M –6391
CT –
U –
N -
M –6419
CT –
U –
N -
Rear Axle
Mer 4.63
Mer 5.57
Mer 5.83
DANA 4.63
DANA 5.57
DANA 5.83

## Slide 31: MBP Models – 4X2 Haulage
L1*R1 - S636OD, 6mm Frame, L1*Suspension
Loading Spans – 18 / 20 / 22 / 24 / 26 / 28 / 32
L2R3 - 6MT86, 7mm Frame, L2 Suspension
Loading Spans – 18 / 20 / 32
L3 / L4 - 8mm Frame, >L2 Suspension
Loading Spans – 18 / 20 / 22
11 inch Frame on all models

## Slide 32: MBP Models – 6X2 MAV
Sub-Segment
Loading Span
Engine Power
GB Config’n
Suspension-Frt
Suspension-Rear
Cab
Fuel Tank
Load Road
200HP H6
SemiEllipt 7000kg
NRS 22000kg
G91 S
220 litres
,
6X2
20 ft
250HP N4
6MT86 8.91
SemiEllipt 8000kg
Slipper End 22T
WIM Eco/ Std
300 litres
L1*R1, L2R1
22 ft
6S 850
Parabolic 7000kg
WSM Eco/ Std/ Dlx
375 litres
L1*R1, L2R1
24 ft
6MT86 8.13
Parabolic 8000kg
L1*R1, L2R1
26 ft
9S1110
L1*R1
28 ft
L1*R1
30 ft
L1*R1, L2R1
32 ft
L1*R1, L2R1
Applications
6X2 Model for POL application will be released separately.
ULW
M –
CT –
U –
N -
M –7542
CT –
U –
N -
M –7570
CT –
U –
N -
M –7698
CT –6650
U –
N -
M –7626
CT –
U –
N -
M -7654
CT –
U –
N -
M –7682
CT –
U –
N -
M –7710
CT –
U –
N -
New FES
Dual Tank
+220Litres
Dual Tank
+300Litres
Dual Tank
+375Litres
Rear Axle
Mer MS15i 5.29
Mer MS15i 5.57
Mer MS15i 6.17
Dana 92S 5.29
Dana 92S 5.57
Dana 92S 6.17
Mer MT149.7 5.29
Dana DSHO44 5.29

## Slide 33: MBP Models – 6X2 MAV
L1*R1 - H6-200HP, 6S850, 7mm Frame till 24ft LS, 8mm Frame for 26ft and above, L1*Suspension
SLE Sus for L1* only
Loading Spans – 20 / 22 / 24 / 26 / 28 / 30 / 32
L2R1 - H6-200HP, 6S850, 7mm Frame till 24ft LS, 8mm Frame for 26ft and above, L1*Suspension
Loading Spans – 20 / 22 / 24 / 26 / 28 / 32
    6MT86, 7mm Frame, L2 Suspension
Loading Spans – 20 / 22 / 24 / 26 / 28 / 32
L2R3 - 6X4, N4-250HP, 9S1110, 8mm Frame, L2 Suspension
Loading Span – 24

## Slide 34: MBP Models – 6X4 MAV
Sub-Segment
Loading Span
Engine Power
GB Config’n
Suspension-Frt
Suspension-Rear
Cab
Fuel Tank
Load Road
200HP H6
G91 S
220 litres
,
6X4
250HP N4
SemiEllipt 8000kg
NRS
22000kg
WIM Eco/ Std
300 litres
L1*R1, L2R1
Bogie 26000kg
WSM Eco/ Std/ Dlx
375 litres
L3R1
24 ft
Parabolic 8000kg
Bogie 38000kg
L2R3
9S1110
Applications
ULW
M –
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
M -
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
New FES
6X4 for Special Applications like Boom Concrete Pump/ Refueller / Truk mounted crane applications will be released separately.
6MT86 8.91
Rear Axle
Mer MT1497 6.5
Mer MT1497 5.57
Mer MT1497 5.83
Mer MT610 7.2

## Slide 35: MBP Models – 6X4 MAV
L2R3 - 6X4, N4-250HP, 9S1110, 8mm Frame, L2 Suspension
Loading Span – 24

## Slide 36: MBP Models – 8X2 TS MAV
Sub-Segment
Loading Span
Engine Power
GB Config’n
Suspension-Frt
Suspension-Rear
Cab
Fuel Tank
Load Road
200HP H6
SemiEllipt 7000kg
NRS 22000kg
G91 S
200 litres
250HP N4
SemiEllipt 8000kg
SlipperEnd 22000kg
WIM Eco/ Std
300 litres
8X2 TS
6S 850
Parabolic 7000kg
WSM Eco/ Std/ Dlx
375 litres
24 ft
Parabolic 8000kg
WSH Dlx
L1*R1, L2R1, L3R1
26 ft
New FES
L1*R1, L2R1
28 ft
L1*R1
30 ft
L1*R1
32 ft
L1*R1, L2R1
Applications
8x2 Model for POL application will be released separately.
ULW
M –
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
M –8839
CT –7700
U –
N -
M –8911
CT –
U –
N -
M –8983
CT –
U –
N -
M –9055
CT –
U –
N -
M –9128
CT –
U –
N -
Dual Tank
+220Litres
Dual Tank
+300Litres
Dual Tank
+375Litres
6MT86 8.91
6MT86 8.13
Rear Axle
Mer MS197 5.83
Dana 92S 5.83
Mer MS197 5.57
Mer MS160 5.57
Dana 92S 5.57

## Slide 37: MBP Models – 8X2 TS MAV
L1*R1 - H6-200HP, 6S850/ 6MT86, 7mm Frame, L1*Suspension,
SLE Sus for L1* only
Loading Spans – 24 / 26 / 28 / 30 / 32
L2R1 - N4-250HP, 6MT86-2, 7mm Frame, L2 Suspension
Loading Spans – 24 / 26 / 28 / 30 / 32
L3R1 - N4-250HP, 6MT86-2, 8+6mm Frame, L2 Suspension
Loading Spans – 24

## Slide 38: MBP Models – 8X2 LA MAV
Sub-Segment
Loading Span
Engine Power
GB Config’n
Suspension-Frt
Suspension-Rear
Cab
Fuel Tank
Load Road
200HP H6
SemiEllipt 7000kg
NRS 22000kg
G91 S
200 litres
250HP N4
SemiEllipt 8000kg
SlipperEnd 22000kg
WIM Eco/ Std
300 litres
8X2 LA
6S 850
Parabolic 7000kg
WSM Eco/ Std/ Dlx
375 litres
24 ft
Parabolic 8000kg
WSH Dlx
L1*R1, L2R1, L3R1
26 ft
New FES
L1*R1,L2R2, L3R2
28 ft
L1*R1, L2R1
30 ft
L1*R1
32 ft
L1*R1, L2R1
Applications
ULW
M –
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
M –8824
CT –7930
U –8160
N -
M –8852
CT –
U –
N -
M –8880
CT –
U –
N -
M –8908
CT –
U –
N -
M –8936
CT –
U –
N -
Dual Tank
+220Litres
Dual Tank
+300Litres
Dual Tank
+375Litres
6MT86 8.91
6MT86 8.13
8x2 Model for POL application will be released separately.
Rear Axle
Mer MS197 5.83
Dana 92S 5.83
Mer MS197 5.57
Mer MS160 5.57
Dana 92S 5.57

## Slide 39: MBP Models – 8X2 LA MAV
L1*R1 - H6-200HP, 6S850/ 6MT86, 7mm Frame, L1*Suspension
      SLE Sus for L1* only
      Loading Spans – 24 / 26 / 28 / 30 / 32
L2R1 - N4-250HP, 6MT86-2, 7mm Frame, L2 Suspension
Loading Spans – 24 / 26 / 28 / 30 / 32
L3R1 - N4-250HP, 6MT86-2, 8+6mm Frame, L2 Suspension
Loading Spans – 24

## Slide 40: MBP Models – 10X2 MAV
Sub-Segment
Loading Span
Engine Power
GB Config’n
Suspension-Frt
Suspension-Rear
Cab
Fuel Tank
Load Road
200HP H6
SemiEllipt 7000kg
NRS 22000kg
G91 S
250HP N4
SemiEllipt 8000kg
SlipperEnd 22000kg
WIM Eco/ Std
10X2 LA
Parabolic 7000kg
WSM Eco/ Std/ Dlx
375 litres
Parabolic 8000kg
WSH Dlx
Parabolic 10500kg
New FES
28 ft
9S 1110
L1*R1, L2R3
30 ft
L1*R1, L2R3
32 ft
L1*R1
Applications
ULW
M -9987 CT -9580 U- 9490 N -9610
M -10046 CT -9630
U -
N -9671
M -10066
CT -
U -
N -9700
10x2 Model for POL application will be released separately.
6MT86 8.91
Final Drive
Mer 5.83
Mer 6.43
Mer 5.63
DANA 5.83

## Slide 41: MBP Models – 10X2 MAV
L1*R1 - H6-200HP/ N4-250HP, 6MT86/ 9S1110, 8mm Frame, L1*Suspension
      SLE Sus for L1* only
      Loading Spans –28 / 30 / 32
L2R3 - N4-250HP, 9S1110, 8+6mm Frame, L2 Suspension
Loading Spans –28 / 32

## Slide 42: MBP Models – 6X4 Tipper
Sub-Segment
Loading Span
Engine Power
GB Config’n
Suspension-Frt
Suspension-Rear
Cab
Fuel Tank
Load Road
200HP H6
NRS 22T
G91 D
220 litres
,
6X4
250HP N4
6MT86 8.91
SemiEllipt L2
Bogie 38T
WDL Eco/ Std
14 CuM
Bogie 48T
L1*R1, L2R1, L2R2, L2R3, L3R2, L3R3, L4R2
16 CuM
Parabolic L2
L1*R1, L2R1, L2R2, L2R3, L3R2, L3R3, L4R2
20 CuM
9S1110
Parabolic >L2
L1*R1, L2R1, L2R2, L2R3, L3R2, L3R3, L4R2, L5R2
20 CuM LWB
L1*R1, L2R1, L2R2, L2R3, L3R2, L3R3, L4R2, L5R2
Applications
ULW
M –
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
M -
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
New FES

## Slide 43: MBP Models – 6X4 Tipper
L1*R1-L2R3 - H6-200HP, 6MT86
L3, L4 N4-250HP, 9S1110, 8mm Frame, Bogie suspension

## Slide 44: MBP Models – 4X2 Tractor
Sub-Segment
Loading Span
Engine Power
GB Config’n
Suspension-Frt
Suspension-Rear
Cab
Fuel Tank
Load Road
4X2 40T
32ft LS
200HP H6
SemiEllipt 7000kg
Semi Ellipt 11500kg
G91 S
L1*R1
4X2 46T
36ft LS
250HP N4
SemiEllipt 8000kg
Semi Ellipt 16000kg
WIM Eco/ Std
300 litres
L1*R1, L2R1
40ft LS
9S 1110
Parabolic 7000kg
WSM Eco/ Std/ Dlx
375 litres
Parabolic 8000kg
New FES
Parabolic 10500kg
Applications
ULW
M –6309
CT –
U –
B –
M –6543
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
6MT86 8.91
Rear Axle
Mer MS149.7 6.17
Mer MS160 6.5
DANA 92S 6.17
DANA HDS 6.83

## Slide 45: MBP Models – 4X2 Tractor
L1*R1 - 6MT86, 7mm Frame, L1* Suspension
Loading Spans – 32 / 36 / 40
L2R1 - 9S1110, 8mm Frame, L2 Suspension
Loading Spans – 32 / 36 / 40
11 inch Frame on all models

## Slide 46: MBP Models – 6X4 Tractor
Sub-Segment
Loading Span
Engine Power
GB Config’n
Suspension-Frt
Suspension-Rear
Cab
Fuel Tank
Load Road
32ft LS
SemiEllipt 7000kg
NRS 22000kg
L1*R1,
6X4 55T
36ft LS
250HP N4
Bogie
26000kg
L1*R1, L2R1, L3R1, L3R2
40ft LS
Parabolic 7000kg
9S1110
Applications
ULW
M – 8078
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
M -
CT –
U –
N -
M –
CT –
U –
N -
M –
CT –
U –
N -
375 litres
G91 S
WIM Eco/ Std
WSM Eco/ Std/ Dlx
New FES
Rear Axle
Mer 6.17
DANA 6.17

## Slide 47: MBP Models – 6X4 Tractor
L1*R1 - 9S1110, 8mm Frame, L1* Suspension
Loading Spans – 32 / 36 / 40
L2R1, L3R1, L3R2 -9S1110, 8mm Frame, L3 BG Suspension
Loading Spans – 3 Axle Trailers 32ft / 36ft / 40ft
11 inch Frame on all models

## Slide 48
Product Add-Ons
Some Additional Product Feature Options
  Headlamp grille
  Cruise control
  Fog Lamps
  DGMS requirements (Rev Prox warning, Rear camera, fire retardant system, etc)
  Centralized Lubrication System
  Tyre pressure monitoring system
  iAlert Advanced
  And others

## Slide 49
Non-Product Add-Ons
Sales Add ons
  Financial assistance
Service Products
  Extended Warranty Package
  Annual Maintenance Contract
  ALCOVER Insurance Package

## Slide 50
Further Plans
May 2019 – Start of On-Road Trials
  Performance Assessment
  Driver acceptance and feedback
  Durability Assessment
  MAV – Max50000 kms covered
  Tipper – Max 2400 hrs covered
  Tractor – Max 500 kms covered
Seeding to select customer
  Primary focus of Applications / Areas based on BS6 diesel availability
  Performance assessment
  Customer feedback
  Customer acceptance
Sale, All India by Q4 of 2019-20
100% BS6 Implementation by 1st April 2020

## Slide 51: THANK YOU