## Slide 1
DRIVER TRAINING
HANDOUT
Updated as on Feb 14, 2020

## Slide 2
  BS6 Fundamentals
    Emission Standard
    Emission Control – AL Approach
  Instrument cluster and Tell-tale
    Understanding the Tell-tale
    Understanding the Tell-tale specific to Exhaust System
      HEST (High Exhaust System Temperature) Lamp
      Regeneration inhibit indication Lamp
        Regen Inhibit Switch
      DPF Lamp
        Parked Regeneration – Precautions, Necessary Conditions, Parked Regeneration Switch
      AdBlue Low level indication Lamp
      NOx Lamp
      MIL Malfunction Indication Lamp
    Understanding Other Tell-tale (Safety and Performance)
      EDC Lamp
      Low air pressure/Brake failure/Park Brake
        Parking Brake Release
      Air filter blocked indicator
      Low Coolant Level warning
      Water in Fuel
    LCD screen navigation
CONTENTS
  Switches and control
    ECU controlled Exhaust brake
      Down hill Driving
    Information on Isolator switch
  Head Lamp High Beam – Better Visibility
  BS6 Diesel & AdBlue
    Tank Cap Locking and Removal Procedure
  Maintaining Fuel Level
  Fuel Economy (Sweet Spot Driving)
  If Vehicle is Not Starting

## Slide 3
% Reduction
(BS I to BS VI)
NOx – 95 %
PM – 97 %
CO – 67 %
HC – 88 %
CO
4.5
HC
1.1
NOx
8.0
PM
0.36
BS I
CO
1.5
HC
0.13
NOx
0.4
PM
0.01
BS VI
CO
1.5
HC
0.46
NOx
3.5
PM
0.02
BS IV
% Reduction
(BS IV to BS VI)
NOx – 88.5 %
PM – 50 %
CO – 0%
HC – 72 %
BS6 – Emission Standard
1.
Huge reduction of Nox, PM and HC

## Slide 4
BS6 – Emission Control – AL Approach
1.
Diesel Particulate Filter where particles (soot) from engines is captured.
Regeneration is the in vehicle cleaning process for Diesel Particulate filter
In the SCR, a pump dozes AdBlue for removing Nox from the Exhaust Gases
Wrong quality of AdBlue can result in Errors in functioning of EATS

## Slide 5
Instrument cluster and Tell-tale
2.

## Slide 6
2.
Low AdBlue warning
High Exhaust System Temperature
DPF regeneration inhibit
DPF Lamp (Regen needed)
MIL
NOx related error
EDC Lamp
Emission
Performance
Stop Lamp
Safety
Low air pressure / Parking brake ON
Instrument cluster and Tell-tale
Critical Alert Tell tale that requires attention from Driver
Air filter blocked indicator
Low coolant level warning
Switches
OFF
ON
Regeneration Inhibit Switch
Press for more than 5 seconds
Parked Regeneration Switch
Low fuel level warning
Air pressure gauges in LCD Screen
Water in Fuel indicator

## Slide 7
Instrument cluster and Tell-tale
Understanding the Tell-tale specific to exhaust system
2.
High Exhaust System Temperature
Condition:
  This indicates regeneration is happening in vehicle
  Regeneration is the cleaning process for Diesel Particulate filter in the Exhaust System
Driver action:
  Drive the vehicle away from flammable substance or heavy traffic immediately
  If above is not possible, press the Regen Inhibit Switch
Effect on vehicle:
  No effect

## Slide 8
Instrument cluster and Tell-tale
Understanding the Tell-tale specific to exhaust system
2.
DPF Regen Inhibit ON
Condition:
  When Regeneration inhibit switch is switched ON by driver due to unfavorable surrounding.
Driver action:
  When Inhibit switch is NOT switched ON and DPF regen inhibit telltale is ON, contact the nearby authorized Ashok Leyland Service Centre.
Regeneration inhibit switch
  When switch is turned ON, DPF regen will be inhibited.
Effect on vehicle:
  No effect

## Slide 9
Regen Inhibit Switch - Usage
Regeneration Inhibit Switch
Inhibit switch is a normal ON/OFF type switch which is used to stop any DPF regeneration (Regeneration can happen on its own while the vehicle is moving or can be initiated by the Driver on a Parked vehicle, when necessary)
It can be used whenever driver foresees any safety concerns during DPF regeneration in flammable environment (eg. fuel filling station / grassy / forest areas where high exhaust temperature can be exposed to flammable materials like dry grass etc. on the ground).
When inhibit switch is ON, inhibit lamp tell tale on dashboard will glow.
Apart from that, LCD message will indicate “Inhibit switch active – DPF regeneration inhibited”.
Do not use inhibit switch unless it is required. Otherwise DPF will accumulate excess soot load over a period of time which will result in Low Pickup and Engine Shutdown in extreme condition. The DPF would require cleaning at authorized Ashok Leyland Service Centre.
OFF
ON

## Slide 10
2.
DPF Lamp
Condition:
  When Diesel Particulate Filter (DPF) is choked and needs regeneration
Driver action:
  Drive the vehicle on a highway at high speed to increase exhaust system temperature.
  If the above condition is not possible, park vehicle in a safe location to start Parked regeneration.
Level 1
DPF lamp solid ON
Effect on vehicle:
  No effect
Instrument cluster and Tell-tale
Understanding the Tell-tale specific to exhaust system

## Slide 11
2.
DPF Lamp
Condition:
  When Diesel Particulate Filter (DPF) is highly choked and parked regeneration has to be carried out at the earliest possible
Driver action:
  Park the vehicle in a safe location to start Parked regeneration immediately.
Level 2
DPF lamp flashing
Effect on vehicle:
  Vehicle pick up would be low when DPF Lamp starts flashing along with EDC lamp ON
Instrument cluster and Tell-tale
Understanding the Tell-tale specific to exhaust system

## Slide 12
Place wheel choke at the front and rear of at least one wheel
Ensure the Fire Extinguisher is at easily accessible location and be aware of using it if required.
During parked regeneration, stay near to the vehicle in order to supervise the procedure and prevent any object or person from coming close to the exhaust.
Verify hood/front opening panel is closed and latched.
Ensure that the exhaust smoke does not come in contact with “dry grass, rags, grease, debris, fuel, oil soaked waste or any flammable substances” and also confirm that no such flammable substance is on or near the exhaust system, during parked regeneration.
FLAMMABLE
FUEL STATION
Precautions before attempting Parked regeneration:
Parked Regeneration - Precautions

## Slide 13
Park the vehicle in a well ventilated area and away from other vehicles.
Ensure gear is in Neutral position
Switch OFF the AC if applicable
Apply Parking Brake - ON
Ensure PTO is switched OFF
Switch ON ignition, START the engine and then START the parked regeneration by pressing the Switch for more than 5 seconds
Engine RPM raises to 2000 RPM when parked regen is started
Do not press Accelerator pedal or any other switches / controls on Dashboard
Keep an eye on vehicle surroundings on all sides when the regeneration is happening
Press for more than 5 sec
Conditions to start Parked Regeneration:
Parked Regeneration – Necessary Conditions

## Slide 14
Parked Regeneration
To activate Parked regeneration, press “START” (bottom side of switch) for more than 5 seconds and release.
To confirm whether parked regeneration activation switch has been pressed properly , please check the LCD message which indicates “Standstill regeneration switch ON” and if Engine RPM raises to 2000 RPM
After that, if all the other parked regeneration enable conditions are satisfied, then LCD message display as “Standstill DPF regeneration active through Switch”.
After that DPF regeneration can also be confirmed through HEST lamp activation.
Parked Regeneration Switch ON
(Lamp Solid ON )
High exhaust system temperature
Press for more than 5 sec

## Slide 15
Parked Regeneration Completion
Once the Regeneration is complete, the Engine RPM drops to Idle RPM.
Both LCD messages, “Standstill regeneration switch ON” and “Standstill DPF regeneration active” will not Display in LCD screen. Also after some time, HEST lamp goes OFF
Parked Regeneration

## Slide 16
2.
DPF Lamp + MIL Lamp + Stop Lamp
Condition:
  When Diesel Particulate Filter is choked completely
Driver action:
  Not safe to drive vehicle. Park the vehicle immediately and contact the nearby authorized Ashok Leyland Service Centre.
Level 3
MIL , STOP Lamp ON and DPF lamp flashing
Effect on vehicle:
  Pick up will be Low and Engine will shutdown after some time when DPF Lamp starts flashing and MIL, red STOP lamp is ON
Instrument cluster and Tell-tale
Understanding the Tell-tale specific to exhaust system

## Slide 17
2.
Low AdBlue Warning
Condition:
  When AdBlue quantity is less than 10 %
Driver action:
  Fill the recommended AdBlue solution immediately.
GULF AdBlue
Level 1
AdBlue warning solid ON
Effect on vehicle:
  No effect
Instrument cluster and Tell-tale
Understanding the Tell-tale specific to exhaust system

## Slide 18
2.
Low AdBlue Warning
Condition:
  When AdBlue quantity is less than 5 % of total filling capacity and Low pick up when the level is less than 2.5%
Driver action:
  Fill the recommended AdBlue solution immediately.
GULF AdBlue
Level 2
AdBlue warning flashing
Effect on vehicle:
  Some time after this tell tale starts flashing, there would be Low Pick up
Instrument cluster and Tell-tale
Understanding the Tell-tale specific to exhaust system

## Slide 19
2.
NOx related Error
Condition:
  DEF (Diesel Exhaust Fluid) Quality might be an issue
  When errors related to Urea Dosing System happens
Driver action:
  Contact the nearby authorized Ashok Leyland Service Centre.
  Ensure only recommended Adblue solution is used.
  Gulf AdBlue
Effect on vehicle:
  Some time after this tell tale glows, there would be Low Pick up
Instrument cluster and Tell-tale
Understanding the Tell-tale specific to exhaust system

## Slide 20
2.
MIL
Condition:
  When MIL glows continuously during engine run, there may be error in Emission control
Driver action:
  Contact the nearby authorized Ashok Leyland Service Centre
Instrument cluster and Tell-tale
Understanding the Tell-tale specific to exhaust system
Effect on vehicle:
Some time after this Tell-tale glows continuously during engine run, there would be Low Pick up.

## Slide 21
2.
EDC Lamp
Condition:
  When there is any abnormality with function of sensors or any electronic components controlled by ECU and Exhaust system
Driver action:
  Contact the nearby authorized Ashok Leyland Service Centre
Effect on vehicle:
  May reduce the Pick-up / Speed or Engine RPM
Instrument cluster and Tell-tale
Understanding the Tell-tale specific to Performance

## Slide 22
2.
Water in fuel
Condition:
  When water gets collected in filter more than allowable limit
Driver action:
  When the telltale starts blinking, drain the water from fuel filter cum water separator mounted on Engine as well as Pre filter mounted on chassis
Effect on vehicle:
  Low Pick up
Instrument cluster and Tell-tale
Understanding the Tell-tale specific to Performance

## Slide 23
2.
Water in fuel
Condition:
  When there is any error, issue in sensor or its wiring connection
Driver action:
  When the tell tale glows continuously, Contact authorized Ashok Leyland Service Centre
Effect on vehicle:
  No effect
Instrument cluster and Tell-tale
Understanding the Tell-tale specific to Performance

## Slide 24
Parking Brake Release
As a product improvement, the Brake system pressure has been increased in all BS6 MDV vehicles. In this new system, the Air Pressure cut out happens between 9.6 and 9.9 bar.
During every Air Pressure cut out (Air release sound), 0.6 bar pressure of air will be used to clean the system on its own and hence this pressure drop is normal.
Low pressure warning Beep sound and Telltale goes OFF when pressure reading in both Front Brake and Rear Brake gauges goes above 5 bar.
When the vehicle is in Parked Condition, the Vehicle cannot be moved immediately after Beep sound and Telltale goes OFF, please wait until pressure reaches 7.9 to 8.1 bar in both the gauges.
Low Pressure warning Beep sound and Telltales and switches ON when any of the gauge reading falls below 4.5 bar.
Air pressure gauges in LCD Screen

## Slide 25
Instrument cluster and Tell-tale
Understanding the Tell-tale specific to Safety
2.
Low Air Pressure / Parking Brake
Effect on vehicle:
  Safety issue and not recommended to drive with Low air pressure telltale ON
Driver action:
Air pressure to be built above 5 bar on both gauges.
Conditions:
When Vehicle is Parked with Hand Brake ON:
Air pressure is less than 4.5 bar in Front or Rear Brake - STOP and Low air pressure Telltale glows together. Also, Beep sound would be audible
Air pressure is more than 5 bar in both the Brakes - Beep sound stops
Driver action:
On MDV BS6 Vehicles, Allow time for the Air pressure to build around 7.9 to 8.1 bar. On other vehicles, wait for the pressure to build around 5 to 5.5 bar. If Air pressure is not building, contact the nearby authorized Ashok Leyland Service Centre
Release the parking brake before moving the vehicle. The STOP and Low Air pressure Telltale goes OFF
When Vehicle is Running:
Air pressure is less than 4.5 bar in Front or Rear Brake - STOP and Low air pressure Telltale glows together. Beep sound also would be audible

## Slide 26
Instrument cluster and Tell-tale
Understanding the Tell-tale specific to Performance
2.
Air Filter Chocked
Condition:
  When Air filter is Chocked
Driver action:
  Visit the nearby authorized Ashok Leyland Service Centre
Effect on vehicle:
  Low Pick up

## Slide 27
2.
Low Coolant Level
Condition:
  When coolant level in DAT is about to reach MIN level
Driver action:
  Check for leakage, arrest and Top up the coolant
  If leakage is not visible, top up the coolant and contact the nearby authorized Ashok Leyland Service Centre
Instrument cluster and Tell-tale
Understanding the Tell-tale specific to Performance
Effect on vehicle:
  Would lead to engine overheating and consequent engine damage if coolant is not topped up immediately

## Slide 28
Instrument cluster and Tell-tale
LCD screen navigation
2.
Contents
Screen 1: Home Page
Screen 2: Vehicle Info
Screen 3: Trip 1
Screen 4: Trip 2
Screen 5: Engine Diagnostics
Screen 6: After Treatment Diagnostics
Screen 7: ABS Diagnostics
Screen 8: Electrical Diagnostics
Screen 9: Warning
Screen 10: Information
Screen 11: Version Info - Cluster
Screen 12: Version Info - BCU
Press MODE button to change the Screens Forward
Press SET button to change the Screens Backward
SET button
MODE button
LCD screen

## Slide 29
Screen 1: Home screen
2.
Time
Date
Instantaneous KMPL
Total Engine Hours
Air pressure gauge 2
Air pressure gauge 1
Gear indicator
Odometer reading (km)
Adblue Level in Percentage
Instrument cluster and Tell-tale
LCD screen navigation
Gear Shift Sweet spot Indication

## Slide 30
Screen 2: Vehicle info screen
2.
The information available in the Vehicle info screen
  OIL PRESSURE in bar
  VEHICLE SPEED in km/h
  BATTERY VOLTAGE in V
Instrument cluster and Tell-tale
LCD screen navigation

## Slide 31
Screen 3: Trip 1 details screen
2.
In Trip 1 details screen, hold SET button to reset the values.
The following information are displayed in the Trip 1 details screen
  DISTANCE covered in km
  FUEL ECONOMY in km/L
Instrument cluster and Tell-tale
LCD screen navigation
SET button

## Slide 32
Screen 4: Trip 2 details screen
2.
In Trip 2 details screen, hold SET button to reset the values.
The following information are displayed in the Trip 2 details screen
  DISTANCE covered in km
  FUEL ECONOMY in km/L
Instrument cluster and Tell-tale
LCD screen navigation
SET button

## Slide 33
Switches and control
Exhaust Brake Actuation
3.
All BS6 Vehicles are equipped with Exhaust Brake. It is fitted after the Turbocharger in Exhaust line.
Exhaust Brake aids in controlling the Engine RPM while driving downhill.
Exhaust Brake is controlled by ECU (Engine Control Unit)
It works on its own at following conditions
When Downhill Support Switch is ON (Provided in Dashboard with symbol)
  It works above 1800 rpm though the Service Brake is not pressed and the Accelerator pedal is not pressed
  When Downhill Support Switch is ON or OFF (Provided in Dashboard with symbol)
  It works above 1500 to 1800 rpm when the Service brake is pressed and the Accelerator pedal is not pressed
  It works above 2650 rpm to 2800 rpm when the Service Brake is not pressed and the Accelerator pedal is in any position (All the telltale blinks at this point and also LCD screen display would be “Apply Brake Immediately”. The Service Brake has to be immediately applied)
Always ensure to switch ON the Downhill Support switch while driving down a slope

## Slide 34
Switches and control
Down Hill Driving
3.
Always ensure to switch ON the Downhill Support Switch in Dashboard with symbol while driving down a slope
While driving the vehicle in long downhill, please drive in same gear that will be used to climb the slope
Ensure not to down shift by more than 1 gear at a time
Ensure not to ride the clutch while you are partially applying the service brake
Apply Service brake as and when required to control the vehicle speed to less than 30 Kmph as well as Engine RPM to be less than 2000 rpm. Downshifting without applying the Service brake could cause the Engine RPM to raise beyond the specified limit and would lead to severe damage to Engine components
You have to immediately apply Service brake when all the telltale flickers, to control Engine RPM

## Slide 35
Isolator switch is located on Back side of Cabin close to Battery on all MDV BS6 Trucks
3.
Switches and control
Isolator Switch
Isolator Switch has to be switched OFF in case of i) any emergency situation involving Electricals or Diesel and ii) long storage of vehicle
Isolator switch has to be switched OFF only after 90 seconds of Ignition Key OFF. If not done so, Exhaust After Treatment System may malfunction / fail and result in Low Torque (The switch shown is in OFF condition)
Isolator switch is located in Dashboard on left side of Instrument Cluster on ICV Bus

## Slide 36
High Beam – Better Visibility
When High beam is selected by Combination switch, all four headlamps will glow in High beam on BS6 MDV trucks.
This will improve the visibility during Night time driving at par with the current field practices
4.

## Slide 37
BS6 Diesel & AdBlue
5.
BS6 Diesel
Please Use Only BS6 Diesel for all Ashok Leyland Trucks and Buses
The amount of Sulphur is reduced by 80% in BS6 diesel (50 ppm to 10 ppm) when compared to BS4 diesel
Usage of BS4 Diesel on BS6 Trucks or Buses would affect the life of DPF in Silencer.
Consequently pick up of vehicle would be affected and result in huge cost of Repair
AdBlue
Please fill only AL recommended AdBlue (Gulf – AUS32)
Fill only the quantity as recommended on RH side of AdBlue tank (48 litres / 24 litres) (Refer Pictures)
Never run the vehicle without AdBlue tank Cap or not closed properly to prevent crystallization of AdBlue.
Never run the vehicle without AdBlue as it will lead to Low Pick up of the vehicle

## Slide 38
BS6 Diesel & AdBlue
5.
Diesel Tank Cap Removal & Fitment
Lift Dust Protection Cap and Insert Diesel tank Key
Rotate the Key
90° Anti-clock wise
Rotate Cap Anti-clock wise to the end & remove from tank
Fix the cap by matching the slot
Rotate Key 90°
Clock wise & remove Key. Rotate the Cap anti clockwise for 2 rotations and verify the cap does not come out
Rotate cap clock wise until it will not rotate further
Removal Step 1
Removal Step 2
Removal Step 3
Fitment Step 1
Fitment Step 2
Fitment Step 3

## Slide 39
BS6 Diesel & AdBlue
5.
DEF Tank Cap Removal & Fitment
Slide the latch and Insert the DEF tank Key
Rotate the Key
90° Anti-clock wise
Rotate Cap Anti-clock wise to the end & remove from tank
Rotate Key 90°
Clock wise & remove Key. Rotate the Cap anti clockwise for 2 rotations and verify the cap does not come out
Rotate cap clock wise until it will not rotate further
Fix Cap by matching the slot
Removal Step 1
Removal Step 2
Removal Step 3
Fitment Step 1
Fitment Step 2
Fitment Step 3

## Slide 40
Maintaining Fuel Level
6.
Low Fuel Level
Condition:
  When Fuel level in Fuel tank reaches 20% of its volume
  The left over volume in Fuel depends on Capacity of tank fitted (i.e., 375 litres capacity tank has the maximum advantage)
Driver action:
  Drive the vehicle to nearest Fuel Station with BS6 Diesel and fill the fuel
  Ensure to fill to avoid Air lock situation
  Ensure only BS6 Diesel is filled, BS4 Diesel will affect the Exhaust After Treatment system
Effect on vehicle:
  If we continue to run the vehicle without filling up BS6 diesel, it would lead to Air lock situation

## Slide 41
Fuel Economy (Sweet Spot Driving)
7.
 | N4 Engine | H6 200HP Engine
Fuel Economy Band | 1200 rpm to 1600 rpm | 1200 rpm to 1600 rpm

## Slide 42
If Vehicle is not Starting
If starter motor works and engine is not starting, check for the following
  Check for fuel availability in Diesel tank
  Remove air lock by using hand primer on Pre- filter mounted on Chassis.
  Check for leak or kink in fuel supply hoses/joints and rectify
  Contact the nearby authorized Ashok Leyland Service Centre.
8.
Vehicle | Location
MDV Trucks | Below Cab Rear end in Co-Driver Side
ICV Trucks | Near Battery Carrier in LHS Frame Side member
MDV and ICV Bus | Inside the Bonnet, close to FIP
If starter motor itself does not crank, check for following
  Condition of Fuses in Main fuse box located in front of Co-driver seat. (Refer Fuse layout sticker on Fuse cover)
  Check for tightness of Battery earth (Ground) connection bolt as follows
  Check for Starter motor earth (Ground) connection in FSM
  Contact the nearby authorized Ashok Leyland Service Centre.
Vehicle | Fuse to be checked
MDV Trucks | F06, F10, FM8 and F34
ICV Trucks | F06
MDV and ICV Bus | F21 (ICV Bus), F47 (MDV Bus)
Vehicle | Battery Earth Location
MDV Trucks | Close to the Battery Carrier
ICV Trucks | Behind Battery Carrier
MDV and ICV Bus | Close to the Battery Carrier

## Slide 43
THANK YOU