## Slide 1: 2620 SERIES 6x2 LA
Best-in-class | Superior Tyre | Higher Reliability & | Better Productivity & | Higher Safety | Choice of cabins | Overall TCO
fluid efficiency | Mileage | Low Maintenance Cost | Performance |  | and loading spans | advantage
2620 HG
2620 HM
2620 HU
2620 HN
BUILD YOUR OWN TRUCK

## Slide 2
SCHEMATIC LAYOUT
H series BS-VI with i-Gen6 technology
147 kW @ 2400 rpm
700 Nm @ 1200 - 1900 rpm
380 mm dia - with air assisted hydraulic booster
6 speed synchromesh gearbox Forged I section - Reverse Elliot type Fully floating, single speed rear axle
Semi-elliptic multi leaf Optional: Parabolic springs
Semi-elliptic multi leaf with parabolic helper springs
HSS material with new improved design
Full air dual line brakes with ABS
Cross linked polymer Capacity: 375 L on LH side
For POL variants: 300 L on RH side
48 L
80 kmph (60 kmph for POL variants)
24 V - 120 Ah (150 Ah for AC Models)
295/ 90 R 20
G - Economy Cowl, M - Economy cabin, U - Value cabin and N - Premium cabin, AC option on U and N variants
Cowl & chassis/ Cabin & chassis
FAW - 7,000 kg; LAW - 7,000 kg; RAW - 11,500 kg; GVW - 25,500 kg
SPECIFICATIONS
Engine type
Max power
Max torque
Clutch
Gearbox
Front axle
Rear axle
Front suspension
Rear suspension
Chassis frame
Brakes
Fuel tank
DEF tank
Max speed
Electricals
Tyres
Cabin
Vehicle configuration options
Chassis weight (Laden)
Specifications & images are indicative and subject to change. Jan’23
MAJOR DIMENSIONS
APPLICATIONS
Market load
e Commerce
Parcel
Logistics
Tanker
Loading span | 7.4 m | 8.1 m | 8.7 m | 9.3 m | 9.7 m
Wheelbase | 5130 mm | 5430 mm | 5880 mm | 5880 mm | 6180 mm
Overall length | 9710 mm | 10360 mm | 10960 mm | 11560 mm | 11960 mm
Turning circle dia | 20.2 m | 22 m | 22.9 m | 23.8 m | 24 m
Overall width | 2570 mm |  |  |  | 
Overall height | M - 2987 mm / U - 3247 mm / N(WIM) - 3177 mm |  |  |  | 
Registered Office - Ashok Leyland Limited, No. 1, Sardar Patel Road, Guindy, Chennai - 600032, Tel. - 91 44 2220 6000
E-mail - reachus@ashokleyland.com | Website - www.ashokleyland.com
AUTHORISED DEALER